Slide 2

Locating a radiating source based on range or range-difference measurements obtained from
a network of passive sensors has been a subject of research over the past two decades
due to the problems importance in many applications.
In this thesis, we develop new solution methods for the problem of localizing a single radiating source based on range and range-difference measurements, that include :
Iterative re-weighting algorithms ;
a penalty convex-concave procedure;
 and sequential convex relaxation procedures .
The primary application area of this work are wireless sensor networks, where the RF signals are used to derive the ranging measurements. However, the solution methods proposed are general and could
be applied to measurements derived from other types of signals.

Slide 3

Geolocation is a rapidly growing field due to the large impact it has on daily life, particularly for real-time navigation on mobile smartphones. Location-based services are playing an increasingly important role in other fields such as teleconferencing, wireless communications, surveillance, and geophysics and many others.

Slide 4

Slide 5

Classical non-survey based localization systems are generally comprised of two
subsystems: range/angle estimation and lateration/angulation .
The range/angle estimation subsystem determines distance or direction between
the mobile object and an array of reference points with known location . The reference points can
be satellites in GPS , or base stations in cellular networks, or a set of iBeacons.
Lateration/angulation subsystem uses the coordinates of the reference points and the distance or angle estimates to find the unknown position.

Slide 6

Time of Arrival localization is based on the fact that
the distance between a mobile device and reference points can be calculated
if the propagation speed of signals is known and the time that a signal takes to be received can be measured.

Slide 7

A TDOA system is comprised of at least three base stations, one of which is the
reference station. All stations are transmitting at precise time intervals, and the
receiver measures the small differences in time that it takes the signals to arrive.
In particular, the set of possible positions of a mobile unit that has a range difference of
d3-d1 from two given base stations BS3 and BS1 is a hyperbola with vertex separation of
d3-d1 and focii located at BS3 and BS1.

Slide 8

Slide 9

Slide 10

Slide 11

Slide 12

Slide 54

The problem in can be (equivalently) written as

The constraints are difficult to satisfy exactly. This motivates a relaxed
set of constraints that lead to the following problem

where γ > 0 is a small scalar, initially set in the range of ∈ (0, 0.5). The solution of
the relaxed problem may be taken as an approximate solution of the constrained problem,
hence the RLS as well. By allowing γ to sequentially and monotonically
decrease to zero, the solution of the relaxed problem converges to that of the constrained
problem, because as γ approaches 0, the feasible regions of two problems become equivalent.
As iterations proceed, the objective will not be monotonically decreasing in general but it will converge to a critical point.

The relaxed problem is nonconvex due to the nonconvexity of the inequality constraints.

Slide 55

To be precise, the first set of constraints are convex, while the second are not.
Because the norm ||kx − a _i^ k|| is a convex function with respect to x, it follows that for
a known x_k, the second set of constraints can be replaced with its affine approximation

Slide 56