Slide 2

Locating a radiating source based on range or range-difference measurements obtained from
a network of passive sensors has been a subject of research over the past two decades
due to the problems importance in many applications.
In this thesis, we develop new solution methods for the problem of localizing a single radiating source based on range and range-difference measurements, that include :
Iterative re-weighting algorithms ;
a penalty convex-concave procedure;
 and sequential convex relaxation procedures .
The primary application area of this work are wireless sensor networks, where the RF signals are used to derive the ranging measurements. However, the solution methods proposed are general and could
be applied to measurements derived from other types of signals.

Slide 3

Geolocation is a rapidly growing field due to the large impact it has on daily life, particularly for real-time navigation on mobile smartphones. Location-based services are playing an increasingly important role in other fields such as teleconferencing, wireless communications, surveillance, and geophysics and many others.

Slide 5

Classical non-survey based localization systems are generally comprised of two
subsystems: range/angle estimation and lateration/angulation .
The range/angle estimation subsystem determines distance or direction between
the mobile object and an array of reference points with known location . The reference points can
be satellites in GPS , or base stations in cellular networks, or a set of iBeacons.
Lateration/angulation subsystem uses the coordinates of the reference points and the distance or angle estimates to find the unknown position.

Slide 6

Time of Arrival localization is based on the fact that
the distance between a mobile device and reference points can be calculated
if the propagation speed of signals is known and the time that a signal takes to be received can be measured.

Slide 7

A TDOA system is comprised of at least three base stations, one of which is the
reference station. All stations are transmitting at precise time intervals, and the
receiver measures the small differences in time that it takes the signals to arrive.
In particular, the set of possible positions of a mobile unit that has a range difference of
d3-d1 from two given base stations BS3 and BS1 is a hyperbola with vertex separation of
d3-d1 and focii located at BS3 and BS1.

Slide 23

Our focus in this chapter will be placed on the localization problem based on range
measurements. We present an algorithm for solving the LS problem at hand based
on a penalty convex-concave procedure that accommodates infeasible
initial points .in solving a fairly large class of nonconvex constrained problems.

Slide 35

Placing such bounds means that as iterations proceed the new iterates (coordinates of possible source locations) are restricted to lie within a physically meaningful region determined by parameters delta

Slide 41

Now we address the localization problems based on range or range-difference measurements.
In both cases we focus on the efficient computation of the least squares estimates .
 We start with converting the unconstrained LS problem to constrained problems.
We then develop solution methods that are inspired by the sequential convex programming based on exact penalty formulation and Taylor expansion.

Slide 43
We begin by re-writing the unconstrained problem in (4.2) as a constrained problem
with second-order cone constraints.
Assume we are in the kth iteration and we are to update the kth iterate.
The increment vector delta are such that the objective function is reduced and,
at the same time, the constraints are better approximated at the next iterate.

Slide 44

We replace the left-hand sides of the above equations with their first-order Taylor approximations

At the same time, at this iteration the objective is written as

Slide 45

Based on the above, the problem to be solved in the k th iteration is formulated as…

The constraints assure that the magnitude of each component in increment vector
is no greater than β. Obviously, this problem is a convex quadratic.
One technical difficulty that may occur in solving it is that the feasible region may be empty.
In such a case the constraints must be adequately relaxed in order for the problem to be solvable.

Slide 46

we relax the problem by introducing nonnegative slack variables,
where the penalty term τ > 0 is a sufficiently large scalar

Slide 47

The input parameters for the algorithm include the bound β on the increment vector.
It controls the size of a ”trust region” over which a convex subproblem
is carried out and is responsible for the performance of the algorithm. If parameter β
is chosen too large, then approximation will perform poorly because in this case
the convex model is less accurate. If β is too small the progress of the algorithm
will be too slow. In our simulations a β between 3 and 6 was found to work very well.

Other input parameters are initial point x 0 , initial weight for penalty terms τ 0 ,
and upper limit of the weight τ max (to avoid numerical problems that may occur if it
becomes too large).

Slide 51

The problem in can be (equivalently) written as

The constraints are difficult to satisfy exactly. This motivates a relaxed
set of constraints that lead to the following problem where γ > 0 is a small scalar, initially set in the range of ∈ (0, 0.5).

By allowing γ to sequentially and monotonically decrease to zero,
the solution of the relaxed problem converges to that of the constrained
problem, because as γ approaches 0, the feasible regions of two problems become equivalent.

As iterations proceed, the objective will not be monotonically decreasing in general but it will converge to a critical point.

The relaxed problem is nonconvex due to the nonconvexity of the inequality constraints.

Slide 52

To be precise, the first set of constraints are convex, while the second are not.
Because the norm ||kx − a _i^ k|| is a convex function with respect to x, it follows that for
a known x_k, the second set of constraints can be replaced with its affine approximation

Slide 53

In this way, in the kth iteration when the iterate x k is known, the nonconvex problem
can be converted to a convex second-order cone programming problem

where the relaxation parameter γ controls the size of the convex hull that defines a
feasibility region, and γ needs to be monotonically decreasing as the iteration proceeds.

And we update the value of gamma linearly or quadratically, where K max is the number of iterations to be executed.